## Slide 1: IPv6
Prof. Ramesh Ragala

## Slide 2: Need for IPv6
IP shortage problem with IPv4 addressing
IPv4 uses 32 bits only  232 addresses only  4 billions
Temporary solutions  CIDR, NAT
IP is used everywhere.  so need of more IP addresses
Problem with NAT:
  It breaks the end to end model
  Slow down the process, while growing NAT
  No easy way of maintain states of NAT, in case of node Failure

## Slide 3: Introduction to IPv6
IETF started work on new version of IP , in 1990
Its major goals are
  Support billions of hosts, even with inefficient address space allocation
  Reduce the size of routing tables
  Simplify the protocol, to allow router to process packets faster.
  Provide better security than current IP.
  Pay more attention to type of service (real time data)
  Aid multicasting by allowing scopes to be specified
  Make it possible for host to roam with out changing its address.
  Allow the protocol to evolve in the future.
  Permit the old and new protocols to coexist for years

## Slide 4: Introduction to IPv6
IETF opened a discussion and suggestion on above goals and IP shortage problem through RFC 1550.
One proposal was, run TCP on CLNP with 160 bits addresses.  but CLNP and IP are some what similar
Another proposed protocol is SIPP (simple Internet Protocol Plus)  selected  called as IPv6
IPv6 meets the above goals fairly well.
It is compatible with like TCP,UDP,ICMP,IGMP,OSPF,BGP and DNS. Not with IP.
Information about IPv6 available in RFC’s 2460 to 2466.

## Slide 5: Introduction to IPv6
IETF opened a discussion and suggestion on above goals and IP shortage problem through RFC 1550.
One proposal was, run TCP on CLNP with 160 bits addresses.  but CLNP and IP are some what similar
Another proposed protocol is SIPP (simple Internet Protocol Plus)  selected  called as IPv6
IPv6 meets the above goals fairly well.
It is compatible with like TCP,UDP,ICMP,IGMP,OSPF,BGP and DNS. Not with IP.
Information about IPv6 available in RFC’s 2460 to 2466.

## Slide 6: Introduction to IPv6
IPv6 has longer addresses than IPv4, 16 bytes long.
IPv6 has simplification of header.  has 7 fields only
IPv6 supports for options.
IPv6 supports big support in security.
IPv6 has more attention paid on Quality of Service.

## Slide 7: IPv6 Header

## Slide 8: IPv6 (cont’d)
The IPv6 fixed header

## Slide 9: IPv4 and IPv6
IP Options
Vers
4
IHL
Type of
Service
Total Length
Identification
Flags
Frag Offset
Time to
Live
Protocol
Header Checksum
Source Address
Destination Address
Source Address
Destination Address
Payload Length
Hop Limit
Next Hdr
Flow Label
Traffic
Class
Vers
6
v4 Header = 20 Bytes + Options
v6 Header = 40 Bytes

## Slide 10: IPv6 Header
Version field  6 for IPv6
Traffic Class
  Used distinguish between the packets with different real time delivery requirements.
  Experiments going on how effectively use this field for multimedia data.
Flow label
  it is also still experimental
  It allows a source and destination to set up a pseudo connection with particular properties and requirements.
  Each flow is designed by source address, destination address and flow number.

## Slide 11: IPv6 Header
Payload Length
  tells how many bytes follow the 48 byte header.
  It is like Total Length filed in IPv4.
Next Header
  It tells the additional (optional) extension headers.
  It simplifies the IPv6 Header.
  It supports up to six extension headers.
  If this header is last, this filed tells that , which transport protocol handler to pass the packet to.
Hop Limit
  Used to keep packets from living forever.
  Works like TTL field in IPv4.

## Slide 12: IPv6 Header
SIP suggest to used 8 byte addresses. But it will ran out in few decades. So they uses 16 byte address
Source Address & Destination Address
  It uses 16 byte to represent address
  It is written as eight groups of four hexadecimal digits with colons between the groups.
  Example
  3ffe:6a88:85a3:08d3:1319:8a2e:0370:7344
  2001:0db8:85a3:08d3:1319:8a2e:0370:7334
IPv4 Address can be written as ::192.16.12.49

## Slide 13: IPv6 Address
IPv4  32 bits  232
IPv6  128 bits  2128

## Slide 14: IPv6 Extension Header
Some time we need the field which we used in IPv4 , those can be introduced in IPv6 in the form of Extension header.
These headers provides extra information and accessed in efficient way.
There are six different types of Extension headers.
These are optional, if there are more than one present, then they have to be followed fixed header in order.
Some header are fixed format :: other headers contains variable length fields  each item is encoded as (Type, Length, Value)

## Slide 15: IPv6 Extension Header
Type is a 1 byte flag telling which option is used
  First 2 bits in Type is used to the router what to do
  The choices are
  1. skip the option
  2.discard the packet
  3.discard the packet and send back the ICMP packet
  4.discard the packet don’t send ICMP packet to multicast address
Length field is also a 1 byte long.
  It tells how long the value is (0 to 255 bytes)
Value field contains any information which is needed (up to 255 bytes)

## Slide 16: IPv6 Extension Header