## Slide 1: Routing Algorithm
Prof. Ramesh Ragala

## Slide 2: Network Layer
Design issues
Routing
Congestion
Internetworking
Internet Protocols
Multimedia or QoS

## Slide 3: Design issues
Goal of layer: get packets from source host to destination host
  Routing: should know about topology of subnet
  Congestion: should avoid overloading some communication lines and routers
  Quality of service: offer the appropriate service
  Internetworking: deal with network differences, if source and destination are connected to different networks

## Slide 4: Design issues
Store-and-forward packet switching
  Equipment of: carrier <> customer
  Algorithm at router
    Receive packet
    Check packet (e.g. checksum)
    Forward packet

## Slide 5: Routing Algorithms
Properties
Shortest Path Routing
Flooding
Distance Vector Routing
Link State routing
Hierarchical routing
Broadcast routing
Multicast routing

## Slide 6: Routing Algorithms
Purpose of Routing
However , all nodes in the network are not directly connected.
Nodes in the network must forward the information to other nodes.
The process of determining where to forward packets and actually doing is called routing.
Session Routing.
Each router has two processes.
1. one process handles incoming packets and forwarding
2. other process update and fill the routing table.

## Slide 7: Routing algorithms
Desirable properties
  Correctness
  Simplicity
  Robustness: able to cope with
    changes in topology, load
    hardware and software failures
  Stability
    Converge to equilibrium
  Fairness
  Optimality
}
all algorithms

hard to achieve
}
conflicting

## Slide 8: Routing algorithms
Desirable properties (cont.)
  Fairness
  Optimality
Conflict!

## Slide 9: Routing algorithms
Taxonomy
  Non adaptive (static Routing)
    Routing decisions computed in advance, off-line and downloaded
  Adaptive
    To changes in
      Topology
      Load
    Get information
      Locally
      From adjacent routers
      From all routers

## Slide 10: Routing algorithms
Principle of Optimality
It is a general statement about optimal route with out regard to network topology or traffic.
It states that, if a router – J is on the optimal path from router – I to router – K, then the optimal path from J to K also falls along the same route.
The set of optimal routes from all sources to a given destination form a tree is called sink tree. The root of the sink is a destination node.

## Slide 11: Routing algorithms
d3 > d2
as
d1 + d3 > d1 + d2
Optimality principle
I 
 K

J
Optimal path from I to K over J
d1
d2
distance
d1 + d2 is minimal
d3
Other path from J to K
Set of all optimal routes
from all sources
to a given destination
is a tree: sink tree

## Slide 12: Routing algorithms
Optimality principle: sink tree
Destination

## Slide 13: Routing: shortest path
Algorithm of Dijkstra: shortest path in graph  static algo
  Graph for a subnet
    Node = router
    Arc = communication line
  Metric
    Number of hops
    Geographic distance
    Mean queuing and transmission delay
Initially, no paths are known, so all nodes are labelled with infinity. These are temporary labels.
As algorithm, proceeds the path found, the label values are changes.  gives the better paths.
Label may be tentative or permanent. Initially all labels are tentative. After applying algorithm, label are permanent.

## Slide 14: Routing: shortest path
Initial node
Elements of algorithm:
Mark all nodes as free: 
Mark initial node as selected: 
repeat till destination is selected:
  Label all free nodes reachable from selected nodes with shortest distance to a selected node
  Select free node with shortest distance to a selected node and mark it as selected

## Slide 15: Routing: shortest path

## Slide 16: Routing: flooding
Every packet is sent out on every outgoing line except the one it arrived at

## Slide 17: Routing: flooding
Every packet is sent out on every outgoing line except the one it arrived at

## Slide 18: Routing: flooding
Every packet is sent out on every outgoing line except the one it arrived at

## Slide 19: Routing: flooding
Every packet is sent out on every outgoing line except the one it arrived at

## Slide 20
if node 1 has a packet to send to node 6, it send a copy of that packet (with a destination address of 6), to nodes 2, 3, and 4.
Node 2 will send a copy to nodes 3 and 4.
Node 4 will send a copy to nodes 2, 3, and 5. And so it goes.
Eventually, a number of copies of the packet will arrive at node 6.
Routing: flooding

## Slide 21
Routing: flooding

## Slide 22
Routing: flooding

## Slide 23
Routing: flooding

## Slide 24: Routing: flooding
Every packet is sent out on every outgoing line except the one it arrived at
Duplicates!! How to limit?
  Hop counter
    Decrement in each router
    Discard packet if counter is 0
    Initialisation?
  Sequence number in packet
    Avoid sending the same packet a second time
    Keep in each router per source a list of packets already seen
Useful?

## Slide 25: Routing: flooding
Every packet is sent out on every outgoing line except the one it arrived at
Sometimes useful
  Robust algorithm: e.g. military applications
  Broadcast
  Comparison purposes: always shortest path
Selective flooding
  Use only those lines that are going approximately in right direction
  Still working?

## Slide 26: Routing: distance vector (Bellman ford algorithm)
Adaptive algorithm
  Exchange of info only with neighbours
Data to be available in each router
  Routing table: per destination
    Distance
    Outgoing line
  Distance to all neighbours
another name  Ford Fulkerson algorithm (1962)
It is developed for ARPANET. Now it is also used in Internet with a name RIP

## Slide 27: Routing: distance vector
Routing table for A
To | cost | via
A | 0 | -
B | 12 | B
C | 25 | B
D | 40 | B
E | 14 | E
F | 23 | E
G | 18 | B
H | 17 | J
I | 21 | E
J | 9 | J
K | 24 | J
L | 29 | J

## Slide 28: Routing: distance vector
Algorithm
  At each step within a router:
    Get routing tables from neighbours
    Compute distance to neighbours
    Compute new routing table
  Characteristics:
    Iterative
    Asynchronous
    Distributed

## Slide 29: Routing: distance vector
Routing tables from

## Slide 30: Routing: distance vector
Better?
Keep 4 tables (one for each neighbour)
Use shortest path

## Slide 31: Routing: distance vector
Distributed algorithm
  Triggers:
    Change in delay to neighbour
    Receive new table from neighbour
  Update local tables
  If changed: forward routing tables to neighbours
Asynchronous
  Execution in lock step not required
Iterative
  Stops?
How fast are changes propagated?
Good news?
Bad news?

## Slide 32: Routing: distance vector
Good news:
A comes up again
Only distances to A
Faster not possible!!!

## Slide 33: Routing: distance vector
Bad news:
A goes down
B receives:
Distance  from A
Distance 2 from C
New distance from B to A: 3 via C

## Slide 34: Routing: distance vector
Bad news:
A goes down
C still
believes its distance to A is 2
routes via B
B routes its packets for A via C
LOOP!!!

## Slide 35: Routing: distance vector
Bad news:
A goes down
Loops!!
Slow!!
 = 5?

## Slide 36: Routing: distance vector
Split horizon hack:
  Lie to neighbour about distance if routing via neighbour
A B C D E
1 2 3 4 initially


lie
 2 3 4 1 iteration
  3 4 2 iterations
   4 3 iterations
Faster not possible!!

## Slide 37: Routing: distance vector
Split horizon hack:
  Hack  does not always work
Example:
  D goes down
  A and B lie to C
  A offers to B route to D
  B offers to A route to D
  Loops again!!!

## Slide 38: Routing: link state routing
Distance Vector Routing protocols are used in ARPANET till 1979.
But it has 2 problems
1. if the delay metric is queue length, it did not take line bandwidth while choosing route.
2. count to infinity problem.
So it is replaced by entire new algorithm is called link state routing protocol.

## Slide 39: Routing: link state
Each router must
  Discover its neighbours and learn their network addresses
  Measure the delay or cost to each of its neighbours
  Construct a packet with these distances
  Send this packet to all other routers
  Compute the shortest path to every other router
The complete topology and all delays are experimentally measured and distributed to every router.
It uses Dijkstra’s algorithm to find shortest paths.
Overview of algorithm:

## Slide 40: Routing: link state
Learning about neighbours:
  Upon boot of router
    Send HELLO packet on each point-to-point line
    Routers are supposed to send reply with a globally unique name
  LAN model
Algorithm:

## Slide 41: Routing: link state
Measuring line cost
  Measure round-trip delay of ECHO Packet and its reply
  Take load into account? Arguments both ways:
Algorithm:
Yes! preference for unloaded line
No! oscillations are possible

## Slide 42: Routing: link state
Building link state packets
  Packet containing:
    Identity of sender
    Sequence number + age
    For each neighbour: name + distance
Algorithm:
When to build?
  periodically
  when significant events occur

## Slide 43: Routing: link state
Distributing link state packets
  Trickiest part of algorithm
    Arrival time for packets different
    How to keep consistent routing tables
  Basic algorithm
    Flooding +
    Sequence number (in each packet) to limit duplicates
  Manageable problems
    Wrap around of sequence numbers:
    Wrong sequence number used:
      lost in case of crash
      Corruption
Algorithm:
32 bits + 1 packet/sec  137 years
Age in each packet:
Decremented during flooding, while used in router
Age 0  info discarded

## Slide 44: Routing: link state
Distributing link state packets
  Basic algorithm
  Manageable problems
  Refinements
    Link state packets are not forwarded immediately
    During holding time:
      duplicates are discarded
      Old packets are thrown out
Algorithm:

## Slide 45: Network Layer
Packet buffer for router B
ACK flag: ACK to send
Send flag: packet to forward

## Slide 46: Routing: link state
Computing new routes:
  With a full set of link state packets, a router can:
    Construct the entire subnet graph
    Run Dijkstra’s algorithm to compute the shortest path to each destination
    Subnet of n router with k neighbours needed storage kn
  Problems for large subnets
    Memory to store data
    Compute time
    Big trouble if any router sends false information.
Algorithm:

## Slide 47: Routing: link state
Usage:
  IS-IS protocol (another link state protocol)
    Designed for DECnet, adopted by ISO
    In use also in Internet
    Supports multiple network layer protocols
  OSPF protocol used in Internet
  Common features:
    Self-stabilizing method of flooding link state updates
    Concept of a designated router on a LAN
    Method of computing and supporting path splitting and multiple metrics

## Slide 48: Hierarchical routing
When network size increases…
  Larger stables
  More CPU time needed to compute …
  More bandwidth needed

## Slide 49: Hierarchical routing
Solution?

## Slide 50: Hierarchical routing
Smaller tables
Longer paths
Routers grouped in regions
Each routers knows how to reach:
  Other routers in its own group
  Other regions
Optimal levels fon N router subnet is ln N requiring a total of e ln N entries per router.

## Slide 51: Broadcast routing
Send message to all other hosts:
  Update distributed database
  Distribute weather reports
  Distribute live radio/TV programs
Poor methods:
  Send a distinct packet to each destination
    List of addresses needed
    High usage of bandwidth
  Flooding
    Too many packets
  Multidestination routing
    Each packet contains a list of destination
    On each line a single packet

## Slide 52: Broadcast routing
Best method: use sink tree
Broadcast source = root of sink tree
Forwarding on sink tree lines
Excellent use of bandwidth
Source tree must be known at each intermediate node
Which sink tree?
How many sink trees?

## Slide 53: Broadcast routing
Sink tree approximation: reverse path forwarding
if a packet arrives on line used for traffic to source of broadcast
then forward packet on all lines, except the one it arrived on
else discard packet

## Slide 54: Multicast routing
Send a message to a well-defined group
  Large in size
  Small compared to network as a whole
Group management
  Create and destroy groups
  Process can leave and join a group
algorithm
How will routers know about groups?

## Slide 55: Multicast routing
Pruning:
  Link state routing
    Each router knows full topology
  Distance vector routing
    Reverse path forwarding +
    PRUNE messages to remove arcs
Algorithm
  Source computes spanning tree
  Remove lines that do not lead to hosts of group ( = pruning)
source

## Slide 56: Multicast routing
Pruning:
  Link state routing
    Each router knows full topology
  Distance vector routing
    Reverse path forwarding +
    PRUNE messages to remove arcs
source

## Slide 57: floyd warshall algorithm
Calculates shortest path between all pairs of nodes in a network.