## Slide 1: Congestion Control in Network Layer
Prof. Ramesh Ragala

## Slide 2: What is congestion? Impact of congestion
When too many packets in the subnet, the performance degrades  called Congestion
the number of pkts dumped into subnet by hosts, must be with in the carrying capacity only. Those are properly delivered to destinations.
Traffic increases  routers are not able to copy all pkts  losing pkts.
@ very high traffic, performance collapses completely and no delivery of pkts.
Max capacity
Congestion controls try to avoid getting into this situation

## Slide 3: Contd...
Reasons :
Suddenly all of pkt are arrived on two or three line and all are send to same output line.  queue is build up  in sufficient memory leads to loss of packets.
  Solution  adding more memory to routers. But Nagle (1987) identified that , infinite memory , congestion get worse.  duplicate
Slow processor are also support the congestion. (queuing buffers, updating the tables etc)
Low bandwidth lines are also causes congestion.

## Slide 4: Contd...
Congestion control Vs Flow Control
Congestion Control
  It’s a global issue
  Whether the subnet is able to carry the offered traffic or not
  It involves the all subnet hosts, all routers , store and forward processing.
Flow Control
  Traffic between sender and receiver only.
  Fast sender not continuously sends the data to slow receiver
  It involves the direct feedback from receiver to sender about regulating traffic.

## Slide 5: General Principles of Congestion Control
Congestion control solutions
Open loop
  It uses good design approach.
  To make sure congestion does not occur in the first place.
  No correction and modification after the system up and running.
Closed Loop
  It is based on Feedback. It has three part
  Monitor the system to detect when and where congestion occurs.
  Pass this information to places where action can be taken.
  Adjust system operation to correct the problem.

## Slide 6: General Principles of Congestion Control
Congestion control solutions
How did the monitoring will takes place.
  It has Varity of metric can be used to monitor the subnet for congestion.
  the percentage of all packets discarded for lack of buffer space.
  the average queue lengths
  the number of packets that time out and are retransmitted.
  the average packet delay
  the standard deviation of packet delay
In second step, it informs about congestion to a point where it can do something do overcome the problem. These pkts are also increases the load at that instance only. Another probe pkt periodically.

## Slide 7: Taxonomy for Congestion Control Algorithms
Open Loop Algorithms
  @ sender side
  @ Receiver Side
  the standard deviation of packet delay
Closed Loop Algorithms
  Explicit feedback Algorithms
  Implicit feedback Algorithms

## Slide 8: Congestion Prevention Policies
Congestion Control by looking up Open loop systems.

## Slide 9: Congestion Control in Virtual Circuits
Dynamically controlled the congestion in Virtual circuits
Admission Control: One the congestion is started, no more virtual circuits setup until the problem gone away.
If any attempts, failure in networks layer.
Another approach, create new virtual paths that should not touch the congestion paths.
Another approach, reserves resources while set up the virtual paths.

## Slide 10: Routing around congestion
(a) A congested subnet. (b) A redrawn subnet, eliminates congestion and a virtual circuit from A to B.

## Slide 11: Congestion control in Data gram subnets
Each router can easily monitor the utilization of its output lines and other resources
Warning Bit:
Router set the warning bit in packet header. Once it receives the destination, it appends the warning bit in ack and sends to the sender. Now sender slow down the data rate.
Choke packets:
In previous approach, warning bit is informed to source in lengthy process. Why can’t the router informs to source.
The router send the CHOKE pkts to source. And it tagged the original pkt not to generate more choke pkts.
The host ignores(queued pkts) the remaining choke pkt from same router for a fixed time period.

## Slide 12: Congestion control in Data gram subnets
Hop by Hop Choke Packets:
Sending choke pkts over long distance is not good.
the choke packet take effect at every hop it passes through.

## Slide 13: Load Shedding
Drop packets when buffers are full
Router can try to drop intelligently
  Dropping older packets is better for multimedia streaming apps
  Dropping newer packets is better for data apps (e.g. file transfer).
    Receiver may discard out-of-order packets
  Dropping use priority classes.

## Slide 14: Random Early Detection
It is well known that dealing with congestion after it is first detected is more effective than letting it gum up the works and then trying to deal with it.
This observation leads to the idea of discarding packets before all the buffer space is really exhausted.
popular algorithm for doing this is called RED (Random Early Detection) (Floyd and Jacobson, 1993).
To determine when to start discarding, routers maintain a running average of their queue lengths
Threshold values

## Slide 15: Jitter Control
(a) High jitter. (b) Low jitter.
The variation in packet arrivals is called jitter