## Slide 1: Network Layer in Internet
Prof. Ramesh Ragala

## Slide 2: Network Layer
Internet can be viewed as collection of sub-networks or Autonomous System.
it provides best efforts to transport layer with out regarding whether the destination in same network or not.
it uses IP protocol.

## Slide 3: IP Protocol
Format of IP datagram.
why we are called datagram?
Datagram  header part + data part
the header part  fixed part + variable part (optional)
fixed part has 20 bytes.
it is transmitted in Big Indian Format  left to right

## Slide 4: The IP Protocol –Header format
The IPv4 (Internet Protocol) header.

## Slide 5: The IP Protocol – header format
Some of the IP options.
5-54

## Slide 6: IP address
IP address are used to address the host in network.
It is unique global address for a network to identify the host and router.
it contains 2 parts
  Host prefix / host portion to specify the n/w
  Network prefix / network portion  specifies the host in n/w
IPv4 contains 32 bit long where as IPv6 has 128 bit long.
It provides 2 services
  Host or network interface identification
  Locating the host
Network bits
Host bits

## Slide 7: Dotted Decimal Notation
Machines read the IP address as a stream of 32 bits.
  The 32-bit address is divided into 4 groups of 8 bits (octet)
  Each octet is written as a decimal no. ranging from 0 to 255.
  The decimal numbers are separated by periods, or dots.

## Slide 8: Subnet mask
The network portion of the address is separated from the host portion of the address by a mask.
it indicating how many bits are used for network portion, by leaving the remaining bits as zero.
24 bit mask /24  24 bits are used for network and remaining 8 bits as host portion.

## Slide 9: Subnet mask

## Slide 10: IP address classification
IP address are classified into 5 categories
  Class – A address
  Class – B address
  Class – C address
  Class – D address
  Class – E address
This is also called Classful addressing.
Private IP addresses  private organization
Public IP addresses  ICANN,ISP’s

## Slide 11: IP Addresses
IP address formats.

## Slide 12: IP address
Class A Networks
  First octet values range from 1 through 126
  First octet starts with bit 0
  Network mask is 8 bits , written /8 or 255.0.0.0.
  1.0.0.0 through 126.0.0.0 are class A networks with 16777214hosts each.
Class B Networks
    First octet values range from 128 through 197
    First octet starts with bit pattern 10
    Network mask is 16 bits , written /16 or 255.255.0.0.
    128.0.0.0 through 191.255.0.0 are class B networks with 65523 hosts each.

## Slide 13: IP address
Class C Networks
  First octet values range from 192 through 223
  First octet starts with bit 110
  Network mask is 24 bits , written /24 or 255.255.255.0.
  192.0.0.0 through 222.255.255.0 are class C networks with 254 hosts each.
Class D Networks
    First octet values range from 224 through 239
    First octet starts with bit pattern 1110
    Class D address are multicast address.

## Slide 14: IP address
0.0.0.0 is a default address, used to specify the default router only.
this 0.0.0.0 address is used by hosts when they are booting.  current n/w
Broadcast address: put all 1’s in host portion  broadcasting in destination network
If you put all 1’s in network and host portion, it pass that packet in all networks.
address beginning with 127 are reserved for internal loopback address.
Class A and B networks very large.
Improve the efficiency of IP addressing.
    Subnet mask
    variable length sub net masks
    Classless interdomain routing.

## Slide 15: IP Addresses (2)
Special IP addresses.

## Slide 16: subnet
Subnet masks are used to
  Creates small networks
  Manage small networks efficiently.
Each router identifying the small sub net by using sub net mask.
the subnet mask borrows some bits from host portion. Due to that we have many network with limited number of hosts.
So IP address have three part  n/w portion + subnet+ host portion.

## Slide 17: Subnetting example
Take class A network 10.0.0.0 with network mask 255.0.0.0
barrow additional 8 subnet bits to network mask.
New subnet mask is 255.255.0.0
New subnets are 10.0.0.0, 10.1.0.0, 10.2.0.0, and so on with 65534 host addresses per subnet. Still too many hosts per subnet
router uses AND operation between the packet address with subnet mask to identify the subnetwork.

## Slide 18: Private and Public IP address
Class A  10.0.0.0 through 10.255.255.255
Class B  169.254.0.0 through 169.254.255.255
Class C  172.16.0.0 through 172.31.255.255
Class D  192.168.0.0 through 192.168.255.255

## Slide 19: CIDR (Classless Internet Domain Routing )
Internet is growing very rapidly.  out of IP address
Many of IP address are wasting. Problem with Class A & B.
Class A has more addresses where as Class-C has very few host address.  not adequate to organizations.
This problem is called Three bearer Problem.
In reality, a class B address is far too large for most organizations.  going for Class C  wasting of IP
sol: split had allocated 20 bits to the class B n/w
problem  routing @ router  more routing tables.

## Slide 20: CIDR (Classless Internet Domain Routing )
One best solution is CIDR.
Define in RFC 1519.
It allocates the remaining IP address in variable- sizes blocks, with out regarding class.
Example : organization needs  2000 IP address
it assigns  2048 IP address.
it is also creating problems while forwarding packets.  because we dropped the classes concepts

## Slide 21: CIDR (Classless Internet Domain Routing )
Process @ router in classful scenario’s
Packet arrived @ Router, copy of the IP address shifted right 28 bits to yield a 4 bit class number.
A 16-way branch then sorted packets into A, B, C, and D (if supported), with eight of the cases for class A, four of the cases for class B, two of the cases for class C, and one each for D and E.
The code for each class then masked off the 8-, 16-, or 24-bit network number and right aligned it in a 32-bit word.
The network number was then looked up in the A, B, or C table, usually by indexing for A and B networks and hashing for C networks.

## Slide 22: CIDR (Classless Internet Domain Routing )
In CIDR this algorithm will not work.
Each routing table entry is extended by giving it a 32-bit mask
So single routing table for all n/w consisting of an array of (IP address, Subnet mask, outgoing link) triples
When a packet comes in, its destination IP address is first extracted.
Comparison takes place on entry by entry.
It is possible that, multiple entries with different subnet mask length. In that case it takes the longest mask. Forward on the link.  this is problem.

## Slide 23: CIDR (Classless Internet Domain Routing )
In CIDR this algorithm will not work.
Each routing table entry is extended by giving it a 32-bit mask
So single routing table for all n/w consisting of an array of (IP address, Subnet mask, outgoing link) triples
When a packet comes in, its destination IP address is first extracted.
Comparison takes place on entry by entry.
It is possible that, multiple entries with different subnet mask length. In that case it takes the longest mask. Forward on the link.  this is problem.

## Slide 24: Continued
RARP
ICMP
DHCP
ARP
Discussed in Class